## Slide 1: Pre-Aerosol, Clouds, and ocean Ecosystem (PACE) Science Team Meeting
20-22 January 2016
Beckman Institute, Cal Tech

## Slide 2: Plankton, Aerosols, Clouds, and ocean Ecosystem (PACE) Science Team Meeting
20-22 January 2016
Beckman Institute, Cal Tech

## Slide 3
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) Mission
Risk | 8705.4 Payload Risk Class C
Launch | 2022/2023, budget and profile driven
Orbit | 97° inclination; ~650 km altitude; sun synchronous
Duration | 3 years
Payload | Ocean color instrument; potential for a polarimeter
LCC | $805M Cost Cap
Science Objectives
Primary: Understand & quantify global aerosol & cloud dynamics, aerosol-ocean interactions, ocean biogeochemical cycling, and ecosystem function due to natural & anthropogenic forcings from environmental/climate variability and change: OCI (expanded SeaWiFS, MODIS heritage)
Primary: Extend key Earth system data records on global ocean ecology, ocean biogeochemistry, clouds, and aerosols (SeaWiFS, MODIS heritage)
Secondary: Understand and resolve/quantify the role of aerosols and clouds in physical climate (the largest uncertainty): polarimeter (MISR heritage)
Applied Sciences: enable carbon monitoring and management, contribute to better weather forecasting, and delineate the impacts of weather events on coastal ecosystems to enable resource management (early returns for ACE mission)
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) is an ocean color, aerosol, and cloud mission identified in the 2010 report “Responding to the Challenge of Climate and Environmental Change: NASA’s Plan for a Climate-Centric Architecture for Earth Observations and Applications from Space Science”.
Notes: 17

## Slide 4
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) Mission Science Team - Timeline and Events
Timeline:
July 2013: ESD Flight Program identifies PACE Science Team Objectives
10 January 2014: Release of Competition for PACE Science Team (ROSES 2013)
10 December 2014: PACE Direction Letter
13 January 2015: PACE Kick-off Meeting (NASA Headquarters)
14-16 January 2015: First PACE Science Team Meeting (UMD Marriott)
21-23 January 2016: Second PACE Science Team Meeting (Cal Tech)
January 2017: Third (and final) PACE Science Team Meeting (TBD)
Threshold Requirements:
  June 2015 - Original due date for PACE Threshold Requirements, conveyed to project in March 2015 – based on SDT report (but backed off SDT report in several areas at project request)
Trade Studies:
  May 2015 – Trade Studies Document conveyed from PACE HQ Program Staff to Project
    Global Ocean Color Sensor – “Ocean Color Instrument”
    Coastal Ocean Color Sensor – “Coastal Camera”
    Atmosphere/Ocean Polarimeter – “Polarimeter”
Notes: 17

## Slide 5
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) – Threshold Requirements (Signed)
Ocean Color Radiometry - ongoing and advanced biological oceanography, ocean ecological, and ocean biogeochemical property estimates from space; coincident observations of aerosols and clouds:
Earth surface spatial resolution at nadir of 1 km2 (pixel dimensions of 1 km x 1 km ±0.1 km along-track) for all bands.
Spacecraft orbit with an equatorial crossing time at or near local noon (1100-1300 window) that is sun-synchronous and polar. Orbit maintenance of ±10 minutes over the lifetime of the mission.
Two-day global coverage of science measurements to solar zenith angle of 75 degrees and sensor view zenith angles not exceeding 60 degrees, with mitigation of Sun glint.
Retrieval of normalized water-leaving reflectance for open-ocean, clear-water conditions and standard marine atmospheres over the wavelength range 350 – 800 nm with 5nm resolution
Normalized water-leaving reflectance retrievals with accuracies of (1) the maximum of either 20% or 0.004 over the wavelength ranges 350 – 395 nm, (2) the maximum of either 5% or 0.001 over the wavelength range 400 – 600 nm, and (3) 10% or 0.002 over the wavelength range 600 – 900 nm.
Inclusion of at least two NIR atmospheric correction measurement bands (one of which should be centered at 865 nm), one NUV measurement band centered near 350 nm, at least four short-wave infrared bands to do cloud measurements, and a measurement band centered at 940 nm.
Downlink of complete 5nm resolution data from spacecraft to ground and archival of full data set
Monthly characterization of instrument detector and optical component changes using lunar observations through the earth viewing port that illuminate all detector elements.
Image striping artifacts, which result from uncharacterized differences in detector responsivity, that are <0.5% and correctable to noise levels (see PACE SDT report for further discussion).
The threshold PACE mission shall have a science phase duration of at least 18 months, with orbit maintenance capability up to 10 years. This includes a twelve-month validation period, which runs concurrently with the science phase.
Notes: 17

## Slide 6
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE)– Threshold Requirements (Signed)
Aerosol & cloud observations made by the OCI, assuming addition of wavelength bands at 940, 1378, 2130, and 2250 nm specifically for cloud measurements to enable continuity of some OMI, MODIS, MISR obs:
Atmospheric Aerosol Measurements
Aerosol Optical Depth
UV at 0.05 or 30% (total)
VIS at 0.05 or 15% (total) over land
VIS at 0.03 or 10% (total) over ocean
b) Fraction of Total Visible Optical Depth contributed by fine mode aerosol over dark water to ±0.25.
Cloud Measurements
Cloud Layer Detection of 5-10% at a cloud optical depth of ~0.3 with dependence on surface type as a partial continuation of MODIS and VIIRS
a) Cloud Top Pressure
Low cloud when optically thick and/or over dark surface at ≤50 hPa
High cloud at >50 hPa.
b) Cloud Water Path as a function of optical depth, effective radius and surface
~30% for liquid clouds
~50% for ice clouds
c) Optical Thickness as a function of optical depth, effective radius, wavelength and surface
~20% for liquid clouds with small sub-pixel heterogeneity
~30% for ice clouds
d) Effective Radius with upper layer weighting
~20% for liquid clouds with small sub-pixel heterogeneity
~30% for ice clouds
Shortwave Radiative Effect at ~10 Wm-2 TOA
Notes: 17

## Slide 7
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE)– Minimum Capabilities for Polarimeter
Minimum performance requirements - ongoing and improved observations of aerosols, clouds, atm corr OC
Spectral Channels (with and without polarization)
Aerosol and Cloud Measurements: Four spectral bands covering the range 400-1600 nm if dense angular sampling is available. Additional band in the 2200 nm window desired if only sparse angular sampling available.
Atmospheric Correction: Four spectral bands covering the range 400-1600 nm.
Uncertainty in Degree of Linear Polarization
Aerosol and Cloud Measurements: Less than 1%
uncertainty.
Atmospheric Correction: Less than 1% uncertainty.
Swath Width
Aerosol and Cloud Measurements: ±15°
Atmospheric Correction: ±25°
Note: may be a function of wavelength (e.g., a narrower
Swath width for UV wavelengths due to high optical depths
at certain higher angle slant paths)
Number of Angles
Aerosol Measurements: 4 view angles selected to
minimize glint contamination.
Ice Cloud Measurements: 5-6 view angles over the required
angular range in at least a single spectral band.
Liquid Water Cloud Measurements: ~50 for cloud bow
Retrievals of droplet size in at least a single spectral band.
Atmospheric Correction: 4 view angles selected to minimize
glint contamination and match ocean color observational
geometries.
Angular Range (at nadir and swath edge)
Aerosol and Cloud Measurements: ±50° view angle range from nadir as measured at the satellite for spectral bands between 400 and 1000 nm.
Atmospheric Correction: ±50° view angle range from nadir as measured at the satellite for spectral bands between 400 and 1000 nm
Pixel Size
Aerosol and Cloud Measurements: 5 km
Atmospheric Correction: 5 km
Radiometric Accuracy
Aerosol and Cloud Measurements: 5%
Atmospheric Correction: 5%
Notes: 17

## Slide 8
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) Mission Science Team – Trade Studies
Global Ocean Color Sensor
  Design drivers
  (1) Lunar calibration through Earth viewing port that illuminates all detectors at the same time, (2) Spectral system degradation tracking involving the minimum number of ‘detector elements’ possible to minimize striping, cross-talk, and other artifacts in instrument level data
  (3) hyperspectral (5 nm) UV-VIS-NIR resolution
  (4) SNR’s consistent with SDT document
  (5) 2-day global coverage
  (6) spectral subsampling at ~1-2 nm resolution from 655 to 710 nm (to enable refined characterization of the chlorophyll fluorescence spectrum).
  Trade/Feasibility Recommendations:
  (1) If the baseline ground resolution for GOCS is 1 km at nadir, evaluate what the highest achievable resolution is that still meets SNR (and other) requirements. This evaluation needs to consider (a) modifications to the baseline design, such as increasing detector-detector integration to increase SNR, (b) changes in mission risk due to higher resolution (e.g., sensor lifetime, increased complexity/optical or electrical components), and (c) changes in cost due to increased data download/handling, design and construction, mass, etc.
  (2) For a given design for the spatial resolution identified in (1) above, evaluate what design options/approaches are available to achieve this resolution at all scan angles. This evaluation needs to consider changes in design, risk, and cost (as above),
  (3) If the baseline UV-VIS-NIR resolution for GOCS is 5 nm from 350 – 800 nm, evaluate design modifications, risks, and costs for (a) expanding this range below 350 nm or to 900 nm and (b) improving resolution to < 5 nm at either all wavelengths or for specific spectral regions.
Notes: 17

## Slide 9
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) Mission Science Team – Trade Studies
2. Coastal Ocean Color Sensor
  Design drivers
  Ocean color measurements near land-ocean interfaces and for specific events (e.g., oil spills, cruise support) at 50 – 100 meter resolution
  (2) Sensor degradation tracking comparable to MODIS Aqua
  (3) ≤20 nm bandwidth spectral measurement bands with center wavelengths at 360 and 380 nm and additional bands consistent with the SeaWiFS at visible and NIR wavelengths
  (4) SNR’s and spatial coverage comparable to OLI on Landsat-8 or HICO.
  Trade/Feasibility Recommendations:
  (1) Evaluate existing sensor designs (space or aircraft heritage) that can achieve instrument/science requirements for COCS. This evaluation needs to consider (a) simplifications to heritage designs that reduce cost or complexity while achieving threshold requirements, (b) changes in mission risk associated with Module 2 and its addition to the mission payload, and (c) changes in cost due to increased data download/handling, design & construction, mass, etc.
  (2) Evaluate alternative sensor designs (i.e., different than heritage sensors) that can achieve instrument/science requirements for COCS. This evaluation needs to consider (a) minimum sensor design requirements to achieve science threshold requirements, (b) changes in mission risk due to addition of the instrument to the mission payload and TRL, and (c) changes in cost due to increased data download/handling, design & construction, mass, etc.
Notes: 17

## Slide 10
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) Mission Science Team – Trade Studies
3. Atmosphere/Ocean Polarimeter
  Recommended Cost Trade Studies
  (1) Inclusion / Addition of bands at 940, 1378, 2250 for cloud property measurements
  (2) Reduction of the uncertainty in DOLP to 0.5%
  (3) Increase swath width to ±30° and ±45°
  (4) Increase the number of measurement angles to 50 and 100
  (5) Increase in angular range to ±70°
  (6) Reduce pixel size to 1 km and 500 m
  (7) Improve radiometric accuracy to 3%
Notes: 17

## Slide 11
Pre-Aerosol, Cloud, and ocean Ecosystem (PACE) Mission Science Team – Trade Studies
4. Additional Trade/Feasibility Studies – SWIR Bands
  Design drivers – Threshold and baseline SWIR measurements with bandwidths, band centers, and SNR requirements as defined by the mission SDT.
  Trade/feasibility Recommendations –
  Evaluate instrument designs modifications necessary to include the threshold and baseline SWIR measurement requirements into the COCS module. This evaluation needs to consider (a) low-risk instrument design options to achieve requirements, (b) changes in mission risk due to addition of the SWIR measurement capability, and (c) changes in cost due to increased data download/handling, design & construction, mass, etc.
  Evaluate instrument designs modifications necessary to include the threshold and baseline SWIR measurement requirements into the GOCS module. This evaluation needs to consider (a) low-risk instrument design options to achieve requirements, (b) changes in mission risk due to addition of the SWIR measurement capability, and (c) changes in cost due to increased data download/handling, design & construction, mass, etc.
  Evaluate instrument design modifications necessary to include the threshold and baseline SWIR measurement requirements into the AOP module. This evaluation needs to consider (a) low-risk instrument design options to achieve requirements, (b) changes in mission risk due to addition of the SWIR measurement capability, and (c) changes in cost due to increased data download/handling, design & construction, mass, etc.
Notes: 17

## Slide 12
Three-year Science Team period (2014-2017)
Theoretical and analytical studies associated with one of two sets of measurements, one for Inherent Optical Properties and the other for Atmospheric Correction.
Risk reduction and further clarify measurement requirements for future collaborative atmosphere and ocean science and applications on the PACE mission are: (1) Inherent Optical Properties (IOPs) of the ocean, specifically the spectral absorption and scattering properties of phytoplankton, nonalgal particles, dissolved organic matter, and seawater itself, and the relationship of these properties to biogeochemical stocks; and (2) Atmospheric Correction of ocean color radiometry, including but not limited to hyperspectral methods, modeling of bidirectional effects and non-negligible radiances in the near-infrared, absorbing aerosols detection, and studies that focus on aerosol and cloud retrievals.
ROSES 2013 A.25: The PACE Science Team

## Slide 13
Each "team" (IOPs and Atmospheric Correction) will be expected to collaboratively produce a final report that details recommended approaches for PACE for their respective measurement suite.
The ultimate goal for each of the two measurement suite teams is to achieve consensus and develop community-endorsed paths forward for the PACE sensor(s) for the full spectrum of components within the measurement suite. The goal is to replace individual ST member recommendations for measurement, algorithm, and retrieval approaches (historically based on the individual expertise and interests of ST members) with consensus recommendations toward common goals.
All proposers were asked to outline methods for implementing their proposed work (as appropriate) into the standard data processing capabilities of the NASA Ocean Biology Processing Group at Goddard Space Flight Center.
The two Science Team leads will need to think about the methods or approaches by which they anticipate bringing the measurement suite groups of the Science Team to consensus.
ROSES 2013 A.25: The PACE Science Team

## Slide 14
Two staff members from NASA’s Goddard Space Flight Center’s Ocean Biology Processing Group and one staff member from NASA’s Langley Research Center designated by the cognizant NASA Headquarters PACE program staff as points of contact for the PACE Science Team activities. These are noncompeted positions, the three (really two) designated people will be full members of the ST, charged to function as the liaison between the ST and the NASA centers that currently handle the data processing and data distribution for aerosol, cloud, and ocean color missions at NASA, respectively. These two designees will participate in all ST activities, including scientific discussions, measurement discussions, algorithm development and retrieval activities, and associated algorithm/retrieval testing and implementation activities (as appropriate). This will be done as a prototyping activity to examine one potential mission data processing approach.
Jeremy Werdell (IOP) and Bryan Franz (Atm Correction); no LaRC rep (yet?)
CCNY/Maria Tzortziou (IOPs and ocean color) and LaRC/Ali Omar (Atmospheric Correction and polarimetry) participate on the ST as applications members. Their goal is to build the applications component of PACE, with support from Mission Applications Rep/Woody Turner - improve fisheries management; monitoring of coastal habitats and HABs; enhance air quality management, tracking smoke, fires, volcanic ash, other airborne plumes; enable carbon monitoring/management; improve weather forecasts; delineate impacts of weather events on coastal ecosystems (resource management)
Incidentally NASA GSFC management have selected Jeremy Werdell as PACE Project Scientist; Bryan Franz has been designated PACE OBPG lead (likely to handle some level of ocean color, aerosol, cloud data from the Ocean Color Instrument)
ROSES 2013 A.25: The PACE Science Team

## Slide 15: Vicarious Calibration & Data Validation
Vicarious Calibration and Data Validation (in situ)
  FY15 – 17: ROSES 2014 A.3*** (update useful?)
    Issued jointly between OBB and ESTO
    Allows lead time for concepts to mature prior to launch
    Identifies technical development needs/risks for the approaches selected
  FY18 – 21: ROSES 2017 (4 years)
    Selects best approach and hardware (pre-launch) or further risk reduction on instrumentation, if needed, for:
      Vicarious calibration of ocean color data products
      Validation of all data products – in situ
      Calibration/validation of polarimetry data products (TBD)
  FY22 – 25: ROSES 2021 (4 years)
    Perform cal/val during mission operations
    Includes airborne and in situ measurements
    Continue every year during mission extensions

## Slide 16: Science Teams Pre-launch and Post-launch
Pre-launch Science Teams
  FY15 – 17: ROSES 2013 A.25
    Covers IOPs and Atmospheric Correction
    Achieves consensus and develops community-endorsed paths forward for the sensor retrievals for the full spectrum of components within a given measurement suite
  FY18 – 21: ROSES 2017 (4 years)
    Allows lead time for scientific algorithm development prior to launch
    Initiates interface between instrument developers and OBPG; OBPG and algorithm developers
    Supports applications research along with research activities
  FY22 – 25: ROSES 2021 (4 years)
    Pre-launch algorithms and post-launch competed science/applications for ocean color instrument’s aerosol, cloud, ocean science, plus aerosol and clouds from polarimeter (TBD)
Post-launch Competed Science - options
  Competed through ROSES 2025
  After launch, joint funding between EOS project, R&A, and PACE mission budget, exploring additional funding from Applied Sciences
  Mission contribution TBD (many bogies)
  Continue during mission extensions

## Slide 17: PACE Applications
NASA ESD completing guidance document for all project applications programs
  Spells out expectations for missions from Pre-Phase A through Phase F
  Should be completed in several weeks
All missions generate applications plans as per the SMAP Mission Applications Plan
  A Phase A activity
Other Phase A applications efforts include: Applications Traceability Matrix (ATM), workshops/reports to inform and build user community, contact list, use cases/case studies
Phase B: launch mission Early Adopters (EA) Program, articulate DAAC support for applied users, updates of Phase A activities
Phases C/D: update applications plan/ATM, EA telecons and case studies, data workshops/short courses, Phase D – baseline report for Senior Review
Phase E: in addition to above – socioeconomic analyses and reports, Senior Review info

## Slide 18: PACE Early Adopters
A subset of external users who have a direct or clearly defined need for new mission data, and who are planning to apply their own resources (funding, personnel, facilities, etc.) to demonstrate the utility of mission data for their particular system or model.
Goal: Facilitate feedback on mission products pre-launch and accelerate the use of mission products post-launch by providing specific and continuous support to Early Adopters who commit to engage in pre-launch applied research.
  The mission will provide Early Adopters with simulated pre-launch data products and/or with planned pre-launch calibration and validation (cal/val) data from mission field campaigns, modeling, and synergistic studies for pre-launch research and provision of quantitative metrics.
  Begin with applications workshops
  Associate each EA with a ST member
  Start applications early!

## Slide 19: PACE Applications Issues
Need regular calls (biweekly?) between PACE Project Science and PACE Applications personnel
Key Issues for Applications to Address this Week
  Coastal Camera Instrument status
  Need for Direct Broadcast?