## Slide 1
Enhancing PACE Multi-Angle Polarimeter Data Products: Deep Neural Networks for Aerosol and Ocean Color Retrieval
Meng Gao
SSAI, NASA Ocean Ecology Lab (616)
Acknowledgment:
NASA: B. A. Franz, K. Knobelspiesse ,B. Cairns, A. Ibrahim, A. Sayer, P. J. Werdell, Y. Hu, et al.
UMBC: P-W. Zhai, X. Xu , V. Martins; SRON: O. Hasekamp
610 SED Director's Seminar, March 3, 2023

## Slide 2: PACE sensors: OCI + 2 MAPs
PACE Orbits, Werdell et al, BAMS (2019)
Ocean Color Instrument (OCI):
  340-890nm
  7 SWIR bands
SPEXone: SRON Spectro-Polarimeter for Planetary Exploration
  385-770nm
  5 angles
HARP2: UMBC Hyper Angular Rainbow Polarimeter
  60 angles: 670nm
  10 angles: 440, 550, 870nm
Notes: HARP2:
Wide swath: nadir 1,556 km
SPEXone:
385-770nm (400 radiance/50 polarization channels)
5 angles: 0°, ±20° and ±58°
Nadir swath 100km

## Slide 3: Multi-angle polarimeter (MAP)
Quiz: where are PACE polarimeters?

## Slide 4: Multi-angle polarimeter (MAP)
Quiz: where are PACE polarimeters?
HARP2(180)
AirHARP (240)
SPEX Airborne
(4050)
SPEXone
(2250)

## Slide 5: Multi-angle polarimeter (MAP)
RSP is used to develop and validate the MAP retrieval algorithm.
HARP2(180)
AirHARP (240)
SPEX Airborne
(4050)
SPEXone
(2250)
APS (4500)
RSP(2763)

## Slide 6: Multi-angle polarimeter (MAP)
Several MAPs are optimized for aerosol studies.
Hyper-angular instrument is optimized for both aerosol and cloud studies.
HARP2(180)
AirHARP (240)
SPEX Airborne
(4050)
SPEXone
(2250)
APS (4500)
RSP(2763)
AirMSPI(99)
POLDER-3(192)
3MI(294)
MAIA(153)
POLDER-1/2
(144)

## Slide 7: PACE common L1C data format
https://oceancolor.gsfc.nasa.gov/data/pace/format/
All three PACE sensors will be co-registered on the ground under a common spatial L1C grids.
Facilitate cross calibration, multiple sensor retrievals, and data synergy.

## Slide 8: MAP helps aerosol retrievals
Improve microphysical properties such as size, refractive index
Assume no uncertainty in measurements

## Slide 9: MAP helps aerosol retrievals
Add uncertainties to measurement.
Notes: HARP2 retrieval cost function
Fine mode effective radius
refractive index (fine)

## Slide 10: But, there are huge computational challenges in MAP processing
2x15 x 7 x 10 x 2s = 60min
Example on RSP retrieval (Gao et al, 2019 AMT, Combine RSP + SPEX )
Retrieval speed per pixel:
Finite difference
wavelength
iterations
Radiative transfer (RT) model
Direct RT calculation
Notes: The parameters include aerosol, mirocphysical parameters, ocean parameters, etc
LUT is too large to be an option (10^15 B ~ 10^6 GB)

## Slide 11: But, NN represents coupled atmosphere and ocean scatterings with high efficiency and accuracy.
2x15 x 7 x 10 x 2s = 60min
Analytical Jacobians
wavelength
iterations
NN RT model
2 x 1 x 10 x 0.01s =0.2s
Retrieval speed per pixel:
NN RT calculation

## Slide 12: But, NN represents coupled atmosphere and ocean scatterings with high efficiency and accuracy.
  Output:
  Reflectance or DOLP
  Input: Geometry, Aerosol, Wind, Chl-a

## Slide 13: What NN can do for PACE MAP retrievals
Forward model (Gao et al, AMT 2021)
Jacobians (Gao et al, Frontiers 2021)
Aerosol optical property calculation (AMT 2021)
Ocean color atmospheric correction (AMT 2021)
Uncertainty (AMT 2022,EGUsphere (preprint))
FastMAPOL

## Slide 14: Large volume synthetic data for production testing
HARP2 L1C simulation | 15 orbits (March 21, 2022)
NN froward model | Fully coupled atmosphere and ocean radiative transfer simulation (Zhai et al, Frontiers, 2022)
L1C geometry/grids | UMBC HARP team and PACE SDS team
Aerosol properties | GMAO MERRA2 reanalysis
Ocean properties | MODIS Ocean color product (Chla)
Part of PACE SDS day in the life test.

## Slide 15: HARP2 L1C DOLP example
+42o
DOLP (440 nm)
March 21, 2022
15 orbits ~10 million pixels
https://oceandata.sci.gsfc.nasa.gov/directdataaccess/Level-1C/

## Slide 16: HARP2 L1C DOLP example
-40o
DOLP (440 nm)
Information on the simulated data for other PACE instruments in L1C format:
https://oceandata.sci.gsfc.nasa.gov/directdataaccess/Level-1C/

## Slide 17: PACE HARP2 L2 retrievals
Data products:
Fine/coarse aerosol properties (size, refractive index, AOD, SSA etc)
Wind speed, Chl-a
Ocean color atmospheric correction (facilitate synergy with OCI)
Uncertainties
More details on MAP data product
https://pace.oceansciences.org/data.htm

## Slide 18: Aerosol optical depth (AOD): Truth
AOD (550 nm)

## Slide 19: Aerosol optical depth (AOD): L2 Retrieval
AOD (550 nm)

## Slide 20: Aerosol optical depth (AOD): L2 Uncertainty
AOD (550 nm)
Uncertainty performance (AMT 2022,EGUsphere (preprint))

## Slide 21: Remote sensing reflectance (Rrs): Truth
Rrs (440nm)

## Slide 22: Remote sensing reflectance (Rrs): L2 Retrieval
Demonstrate atmospheric correction on HARP2 data
Assist hyperspectral PACE OCI atmospheric correction
Rrs (440nm)

## Slide 23: Summary
We can process HARP2 data over ocean if PACE launch tomorrow.
Further improvement
  Retrieval performance
  Multi-angle data for cloud mask and ocean color
  Integration with production system